10 mm Rockpanel Lines² S & XL

A Rockpanel product with a shiplap profile that is suitable for soffit and fascia applications.

The boards are secret-fixed using stainless steel nails.

The material is available in 10 colours with the options of a primed and natural finish. The natural finish requires no treatment and will darken in a non-uniform manner depending on environmental conditions.

Maximum lead time is 2 weeks.

10 mm Rockpanel Lines² can only by used in ventilated constructions.

950 FASCIAS/BARGES/SOFFITS: PRE-FINISHED STONEWOOL BOARD:

(Please delete clauses in red to suit specification)

Product reference: 10 mm Rockpanel Lines² S & XL

Material: Inert Rockwool panels with pre-finished decorative coating

Manufacturer: Rockwool BV / Lapinus, Industrieweg 15

6045 JG Roermond, The Netherlands

Sales Representative: Rockwool BV / Group Rockpanel, Wern Tarw, Pencoed, Bridgend CF35 6NY.

Tel: 01656 863210.  Fax: 01656 863611.

E-mail: info@rockpanel.co.uk.  Web: www.rockpanel.co.uk.

Thickness: 10mm

Finish: Standard

Board dimensions:

S: 3050x164 mm wide (working width = 146 mm)

XL: 3050 x 295 mm wide (working width = 277 mm)

Colour:

Pure White RAL 9010 / Light Ivory RAL 1015 / Cream White RAL 9001 / Signal grey RAL 7004  / Anthracite Grey RAL 7016 / Primed finish / Natural

Accessories:

Rockpanel profile K: Aluminium starter trim

Joints

Type/treatment:

Vertical joint treatment

Flexible joint Gasket EPDM weather and UV resistant at vertical board joints

(for example; ref 090/60P of Plastestrip)

Colour: Black

Flexible joint Gasket EPDM weather and UV resistant at intermediate supports

(for example; ref 090/36P of Plastestrip)

Colour: Black

Flexible joint Gasket EPDM weather and UV resistant at vertical corner joints

(for example; ref 090/750P of Plastestrip)

Colour: Black

Note: Gaskets are fixed to increase longevity of timber battens and must be used.

### External Corner Treatment

Rockpanel profile D: External corner profile (aluminium) for 10 mm board.

Colour: Colour matched to board / Black / White.

Rockpanel Profile E: External caped corner profile (aluminium) for 10 mm board.

Colour: Colour matched to board / Black / White.

Optional:

Soffit strip ventilator for 10,000 MM² /M Air Flow for example Ref:055/10K

Colour: Colour matched to board / Black / White

Soffit strip ventilator for 25,000 MM² /M Air Flow    for example Ref:085/25L

Colour:  Colour matched to board / Black / White.

Manufacturer: Plastestrip (Profiles) Ltd, 1 Enterprise Park, St Austell, Cornwall, PL25 4EJ.

Tel: 01726 74771. Fax: 01726 69238.

E-Mail: sales@plastestrip.com Web: www.plastestrip.com

Other requirements:

No gaskets required on sofft boards, providing fascia board extends 7.5mm beyond the soffit board.

Construction: 10 mm Rockpanel Lines² can only by used in ventilated constructions.

Board joints:	Fascias & soffits – Maintain a 3-5mm gap on all vertical joints.

Junction of the soffit board and the fascia maintain a gap of 5mm.

Junction of Soffit and Wall: Maintain a 5mm gap.

Support:

10 mm thick Rockpanel boards

50mm x 38mm softwood timber at maximum 600mm centres with 75 x 38mm timber at vertical board joints.  All timber to be treated to Clause G20 270

Fixings:

Fix with Rockpanel ring shank nails 2,1/2,3 x 27 mm, stainless steel AISI 316, at maximum spans of 600mm.  The centre line of the nail fixing should be 11-12mm from the top edge of the board.

Please consult Rockpanel BV for wind loading calculations.

270 Ungraded Softwood for Fascia, Soffit and Barge supports.

- Quality of timber: free from decay, insect attack (except pinhole borers) and with no knots wider than half the width of the section.

- Surface finish: PSE

- Treatment: C2