G20 CARPENTRY/TIMBER FRAMING/FIRST FIXING

950 FASCIAS/BARGES/SOFFITS: PRE-FINISHED STONEWOOL BOARD:

Rockwool Rockpanel.

Formed from compressed rockwool with thermo-hardening synthetic binding compounds to produce a “dimensionally stable” vapour permeable panel that can be fixed in a ventilated or non-ventilated (sealed) construction. Rockpanel Lines can only be used in ventilated constructions. For use in non-ventilated constructions, please contact Rockwool BV/ Rockpanel Group for advice.

Rockpanel products are water repellent and inherently “fire safe”, not propagating fire.  They achieve Class “O” as defined in the Building Regulations or as class B-S2-D0 due to the European fire classification.

Rockpanel boards can be curved – minimum of radius of 1900mm – 6mm boards and 2500mm – 8mm boards.  Particular attention must be given to the position of the fixings when fixing the boards to a curved structure – contact Rockwool BV/ Rockpanel Group for details.

Rockpanel products may be fixed to timber battens, without the necessity for “pre-drilling” using stainless steel Torx screws or stainless steel ringshank nails, both with colour-matched heads

Rockpanel products can also be fixed to aluminium or galvanised steel support rails.  Rockpanel products may be cut on site with normal woodworking tools, however for large areas Rockwool  BV/ Rockpanel Group recommends a fine cut, 64 tooth TCT blade.

Rockwool  BV/ Rockpanel Group sells 5 fascia, Soffit and barge detail products.

## Rockpanel Rockclad

### Rockpanel Structure

#### 10 mm Rockpanel Lines² S & XL

##### 8 mm Rockpanel Lines² S & XL

###### Rockpanel Woods