Rockpanel Natural

The surface gives a natural ageing effect due to UV light, the appearance of the ageing pattern cannot predict as this is the result of the actual environment and detailing, even at micro level.

Board dimensions: 3050 x 1200mm

Board thickness: 8 & 10mm

Available in a choice of durable – for general applications or Xtreme – for applications where greater mechanical strength is required and suitable for ground level installations.

Rockpanel Natural has been awarded with an ETA certificate.

Rockpanel Natural is recommended for ventilated constructions as this results in the most desired ageing patterns. For more information on natural aging, please contact Rockpanel BV for advice.

(Please delete Clauses in red to suit specification)

150 RIGID SHEET CLADDING…………

Product reference:

Rockpanel Natural Durable board

Rockpanel Natural Xtreme board

Material: Inert Rockwool panels without pre-finished decorative coating

Manufacturer: Rockwool Lapinus Productie BV, Industrieweg 15

6045 JG Roermond, The Netherlands

Sales Representative: Rockwool Rockpanel BV, Wern Tarw, Pencoed, Bridgend CF35 6NY.

Tel: 01656 863210.  Fax: 01656 863611.

E-Mail: info@rockpanel.co.uk.  Web: www.rockpanel.co.uk.

Thickness: 8mm or 10mm

Finish: Without any finish

Colours: Natural which discolour (mostly darkens considerable) after several months depending on the environment

# Fixings:

# For Aluminium:

# Aluminium (AlMg5)Rivet with colour match head minimum Ø 14mm, length 18 mm and shank diameter 5 mm.	Pre-drill Rockpanel with 9mm holes and 5.5mm for centre fixings.  A spacer tool should be used when fixing rivets.

# Ref: RP/fix 20 Stainless steel (A4 grade) self tapping screws (thickness aluminium between 1,2 and 2,5 mm) with colour matched heads. Please note when using self tappers the maximum panel size is 1500 x 1200mm.

# For Steel:

# Ref: RP/fix 20 Stainless steel (A4 grade) self tapping screws with colour matched heads.

Ref:	River/spacer tool

Number and location:

Rivets and self tappers to be fixed at a maximum span of 400 mm and maximum 300 mm vertical centres by a 8mm board, and maximum span of 600 mm and maximum 600 mm vertical centres by a 10 mm board.

Please consult Rockpanel BV for wind loading calculations

Fixings to be positioned minimum 15mm from the vertical edge of the board and minimum 50mm from the horizontal edge of the board.

Joints

Type/treatment:

Vertical joint treatment:

If desired, blackout tape can be applied to prevent light reflection from aluminium supports.

### Horizontal joint treatment

8mm boards

Rockpanel profile A: Aluminium horizontal chair section (with high back)

Rockpanel profile B: Aluminium horizontal V-bird section

10mm boards

Rockpanel profile A: Aluminium horizontal chair section (with high back)

Rockpanel profile B: Aluminium horizontal V-bird section

### External Corner Treatment

8mm boards

Rockpanel profile D: External corner profile (aluminium)

Rockpanel profile E: External capped corner profile (aluminium)

10mm boards

Rockpanel profile D: External corner profile (aluminium)

Rockpanel profile E: External capped corner profile (aluminium

Distance between boards: Minimum of 6mm

Air gap:  Minimum 25mm –

Consult Rockpanel for recommendations and details if designing to NHBC requirements

In accordance with ETA Approval for example:

Secondary support system/framing system;

Product reference:	Plastestrip Top Hat and Z profile system

Material:	Aluminium

26mm cavity

Ref: AL/TH/26/50 - Top Hat Profile

Ref:AL/Z/26/50/26 - Z profile

40mm cavity

Ref: AL/TH/40/55 - Top Hat Profile

Ref:AL/Z/40/55/26 - Z profile

#### Fixings: number and location

Consult with Plastestrip for recommendations and details

For cavities greater than 40mm – 270mm contact Plastestrip for further details

Thermal Insulation: As clause H92 775

Breather membrane:	As clause H92 785

Rockpanel Accessories:

### Bottom Drips

Rockpanel profile J: aluminium bottom drip profile

General Accessories:

Ventilated profiles:

Ref: 025/10K	bottom vent strip – 25mm cavity

Ref: 065/10K	bottom vent strip – from 30-65mm cavities

Ref: 090/25K	bottom vent strip – from 65-90mm cavities

Ref: 125/25K	bottom vent strip – from 90-125mm cavities

Manufacturer: Plastestrip (Profiles) Ltd, 1 Enterprise Park, St Austell, Cornwall, PL25 4EJ.

Tel: 01726 74771. Fax: 01726 69238.

E-Mail: sales@plastestrip.com Web: www.plastestrip.com

# GENERAL REQUIREMENTS

- CONTROL SAMPLES

- General: Complete an area of the cladding and obtain

approval of appearance before proceeding.

  - Location :……….

  - Extent of area……….

- FIXING SHEETS

- General: Secure to supports without producing distortion.

- Fasteners: Evenly spaced in straight lines, in pairs across

joints and sufficient distance from edge of sheet to prevent

damage.

- COVER STRIPS

- General: Form straight runs in single lengths wherever possible

- Location and method of forming joints: Submit proposals where

not detailed.