Rockpanel Chameleon

A Rockpanel surface treated with four layers of water-based acrylic coating and a two-component end layer with ProtectPlus as standard. Chameleon is available in a range of 4 standard colours/ effects. The surface has excellent UV resistance when tested in accordance with ISO 4893-1&2 and judged in accordance with ISO 105-A02 and ISO 105-A03. Rockpanel Chameleon can only be used in ventilated constructions.

Board dimensions: 3050 x 1200mm

Board thickness: 8 mm

Available in a choice of durable for general applications or Xtreme for applications where greater mechanical strength is required.

Protect plus finish is standard which improves UV protection and provides anti-graffiti and self-cleaning finish.

Rockpanel Chameleon has been awarded with several ETA certificates.

All Rockpanel standard products have a maximum lead time of 2 weeks.

Please consult Rockpanel BV for advice on use of other Rockpanel Metallic’s cladding products in non-ventilated constructions.

(Please delete clauses in Red to suit specification)

155 SHEET CLADDING ……………

Product reference:

Rockpanel Chameleon Durable board

Rockpanel Chameleon Xtreme board

Material: Inert Rockwool panels with colour changing Characteristics.

Manufacturer: Rockwool Lapinus Productie BV, Industrieweg 15

6045 JG Roermond, The Netherlands

Sales Representative: Rockwool Rockpanel BV, Wern Tarw, Pencoed, Bridgend CF35 6NY.

Tel: 01656 863210 Fax: 01656 863611.

E-Mail: info@rockpanel.co.uk.  Web: www.rockpanel.co.uk.

Thickness: 8mm

Finish: Protect Plus as standard

Colours:

# Purple-Green-Blue / Light Purple-Light Brown / Red-Gold-Purple / Orange-Green-Brown

# Fixings:

# Rockpanel Torx screw:

Stainless steel torx head A1S1 316 grade 4.5x35mm screws, according ETA approval with either a matt black or stainless steel finish.

Rockpanel ring shank nail:

Ring shank A1S1 316 grade stainless steel 2.7/2.9 x32 mm (flat head) nails, according ETA approval with either a matt black or stainless steel finish.

Number and location:

8mm boards

Torx head screws fixed at maximum spans of 600mm and 600mm vertical centres.

Nails to be fixed at maximum spans of 600mm and 400mm vertical

centres.

Please consult Rockpanel BV for wind loading calculations

Fixings to be positioned minimum 15mm from the vertical edge of the board and minimum 50mm from the horizontal edge of the board.

Joints

Type/treatment:

Vertical joint treatment

Flexible Joint Gasket weather and UV resistance at vertical board joints (for example ref: 090/60P of Plastestrip)

Colour: Black

Flexible Joint Gasket weather and UV resistance at intermediate supports (for example ref: 090/36P of Plastestrip)

Colour: Black

Flexible Joint Gasket weather and UV resistance at vertical corner joints (for example ref: 090/75P of Plastestrip)

Colour: Black

Note: Gaskets are fixed to increase longevity of timber battens and must be used.

### Horizontal joint treatment

8mm boards

Rockpanel profile A: Horizontal chair section (with high back) for 8mm board (aluminium)

Rockpanel profile B: Horizontal V-bird section for 8 mm board (aluminium)

### External Corner Treatment

8mm boards

Rockpanel profile E: External capped corner profile (aluminium)

Rockpanel profile D: External corner profile (aluminium)

Colour: Colour matched to board/Black/White

Manufacturer: Plastestrip (Profiles) Ltd, 1 Enterprise Park, St Austell, Cornwall, PL25 4EJ.

Tel: 01726 74771. Fax: 01726 69238.

E-Mail: sales@plastestrip.com Web: www.plastestrip.com

Distance between boards: 5mm

Air gap:  Minimum 25mm –

Consult Rockpanel for recommendations and details if designing to NHBC requirements

Support system: Timber battens as clause 230

Size: Min 75mm wide x 38mm deep at boards joints.

Min 50mm wide x 38mm deep at intermediate supports.

(Above timbers can be planed down to 70mmx28mm and 45mmx28mm respectively)

#### Fixings: number and location

Consult with Rockpanel for recommendations and details

Accessories:

Ventilated profiles:

Ref: 065/10K	bottom vent strip – from 30-65mm cavities

Ref: 090/25K	bottom vent strip – from 65-90mm cavities

Ref: 125/25K	bottom vent strip – from 90-125mm cavities

### Bottom Drips

Rockpanel profile J: aluminium bottom drip profile – 8mm board

Manufacturer: Plastestrip (Profiles) Ltd, 1 Enterprise Park, St Austell, Cornwall, PL25 4EJ.

Tel: 01726 74771. Fax: 01726 69238.

E-Mail: sales@plastestrip.com Web: www.plastestrip.com

# GENERAL REQUIREMENTS

- CONTROL SAMPLES

- General: Complete an area of the cladding and obtain

approval of appearance before proceeding.

  - Location: ……….

  - Extent of area: ……….

- TIMBER BATTENS

- General: Regularized softwood tree from decay, insect attack (except ambrosia beetle damage) and with no knots wider than half the width of the section

- Preservative treatment: As section Z12 and Wood Protection Association Preservative Treatment Commodity Specification C8.

- Type: ……………

- Moisture content at time of fixing (maximum): 19%

- TREATED TIMBER

- Exposed cut and drilled surfaces: Treat with two flood coats of a solution recommended for the purpose by main treatment solution manufacturer.

- FIXING SHEETS

- General: Secure to supports without producing distortion.

- Fasteners: Evenly spaced in straight lines, in pairs across joints and sufficient distance from edge of sheet to prevent damage.

- COVER STRIPS

- General: Form straight runs in single lengths wherever possible

- Location and method of forming joints: Submit proposals where

not detailed.